## Slide 1: CSE 31 Computer Organization
Lecture 20 – Caches (2)

## Slide 2: Announcement
Lab #9 this week
  Due in one week
Project #2 out Friday
  Due Monday (12/3)
    Don’t start late, you won’t have time!
Reading assignment
  Chapter 5.1 – 5.6 of zyBooks (Reading Assignment #6)
    Make sure to do the Participation Activities
    Due Monday (11/26)

## Slide 3: Announcement
Midterm Exam 2
  11/28 (Wednesday, in lecture) Not 11/7 as scheduled
  Lectures #8 - #18
  HW #3 - #5
  Practice exam in CatCourses
  Closed book
  1 sheet of note (8.5” x 11”)
  MIPS reference sheet will be provided

## Slide 4: Typical Memory Hierarchy
Second
Level
Cache
(SRAM)
Control
Datapath
Secondary
Memory
(Disk
Or Flash)
On-Chip Components
RegFile
Main
Memory
(DRAM)
Data
Cache
Instr
Cache
Speed (cycles): ½’s 1’s 10’s 100’s 1,000,000’s
Size (bytes): 100’s 10K’s M’s G’s T’s
Principle of locality + memory hierarchy presents programmer with as much memory as is available in the cheapest technology at the speed offered by the fastest technology
Cost/bit: highest lowest
Notes: Instead, the memory system of a modern computer consists of a series of black boxes ranging from the fastest to the slowest.
Besides variation in speed, these boxes also varies in size (smallest to biggest) and cost.
What makes this kind of arrangement work is one of the most important principle in computer design. The principle of locality. The principle of locality states that programs access a relatively small portion of the address space at any instant of time.
The design goal is to present the user with as much memory as is available in the cheapest technology (points to the disk).
While by taking advantage of the principle of locality, we like to provide the user an average access speed that is very close to the speed that is offered by the fastest technology.
(We will go over this slide in detail in the next lectures on caches).

## Slide 5: Direct-Mapped Cache (4/4)
What should go in the tag?
  Do we need the entire address?
    What do all these tags have in common?
Why not count by cache #?
  It’s useful to draw memory with the same width as the block size
0 | 1 | 0
2 | 3 | 2
4 | 5 | 4
6 | 7 | 6
8 | 9 | 8
A | … | …
C |  | 
F |  | 
10 |  | 
12 |  | 
14 |  | 
16 |  | 
18 |  | 
1A |  | 
1C |  | 
1E |  | 
Memory
Memory address
0 | 8 |  | 
1 | 2 |  | 
2 | 14 |  | 
3 | 1E |  | 
8-byte Direct-mapped cache w/ Tag
Cache index
Block size = 2 bytes
Tag
Data
0
1
2
3
--- 1
--- 0
--- 2
--- 3

## Slide 6: Issues with Direct-Mapped
Since multiple memory addresses map to same cache index, how do we tell which one is in there?
What if we have a block size > 1 byte?
  Answer: divide memory address into three fields
t t t t t t t t t t t t t t t t t t | i i i i i i i i i i | oooo
Tag to check if it has the correct block
Index to select block
Byte offset within block

## Slide 7: Direct Mapped Cache Example
One word blocks, cache size = 1K words (or 4KB)
20
Tag
10
Index
Data
Index
Tag
Valid
0
1
2
.
.
.
1021
1022
1023
31 30 . . . 13 12 11 . . . 2 1 0
Byte offset
What kind of locality are we taking advantage of?
20
Data
32
Hit
Valid bit ensures something useful in cache for this index
Compare Tag with upper part of Address to see if it’a Hit
Read data from cache instead of memory if a Hit
Notes: Let’s use a specific example with realistic numbers: assume we have a 1 K word (4Kbyte) direct mapped cache with block size equals to 4 bytes (1 word).
In other words, each block associated with the cache tag will have 4 bytes in it (Row 1).
With Block Size equals to 4 bytes, the 2 least significant bits of the address will be used as byte select within the cache block.
Since the cache size is 1K word, the upper 32 minus 10+2 bits, or 20 bits of the address will be stored as cache tag.
The rest of the (10) address bits in the middle, that is bit 2 through 11, will be used as Cache Index to select the proper cache entry
Temporal!

## Slide 8: Caching Terminology
When reading memory, 3 things can happen:
  cache hit:
    cache block is valid and contains proper address, so read desired word
  cache miss:
    nothing in cache at appropriate block, so fetch from memory
  cache miss, block replacement:
    wrong data is in cache at appropriate block, so discard it and fetch desired data from memory (cache always copy)

## Slide 9: Caching: A Simple First Example
00
01
10
11
Cache
Main Memory
Q: Where in the cache is the mem block?
Use next 2 low order memory address bits – the index – to determine which cache block (i.e., modulo the number of blocks in the cache)
Tag
Data
Q: Is the mem block in cache?
Compare the cache tag to the high order 2 memory address bits to tell if the memory block is in the cache
Valid
0000xx
0001xx
0010xx
0011xx
0100xx
0101xx
0110xx
0111xx
1000xx
1001xx
1010xx
1011xx
1100xx
1101xx
1110xx
1111xx
One word blocks
Two low order bits define the byte in the word (32b words)
(block address) modulo (# of blocks in the cache)
Index
Notes: For lecture
Valid bit indicates whether an entry contains valid information – if the bit is not set, there cannot be a match for this block

## Slide 10: Direct Mapped Cache
Address 0
Consider the main memory word reference string
  0 1 2 3 4 3 4 15
Start with an empty cache - all blocks initially marked as not valid
0000 0001 0010 0011 0100 0011 0100 1111
Notes: For class handout

## Slide 11: Direct Mapped Cache
0
Consider the main memory word reference string
  0 1 2 3 4 3 4 15
00 Mem(0)
miss
Start with an empty 4-word cache - all blocks initially marked as not valid
  1 requests, 1 miss
0000 0001 0010 0011 0100 0011 0100 1111
Notes: For lecture
Reference string is word addresses (or block number since we are using one word blocks) – i.e., the low order two bits used to selected the byte in the 32-bit word are ignored

## Slide 12: Direct Mapped Cache
0
1
2
3
4
3
4
15
Consider the main memory word reference string
  0 1 2 3 4 3 4 15
00 Mem(0)
00 Mem(0)
00 Mem(1)
00 Mem(0)
00 Mem(0)
00 Mem(1)
00 Mem(2)
miss
miss
miss
miss
miss
miss
hit
hit
00 Mem(0)
00 Mem(1)
00 Mem(2)
00 Mem(3)
01 Mem(4)
00 Mem(1)
00 Mem(2)
00 Mem(3)
01 Mem(4)
00 Mem(1)
00 Mem(2)
00 Mem(3)
01 Mem(4)
00 Mem(1)
00 Mem(2)
00 Mem(3)
01
4
11
15
00 Mem(1)
00 Mem(2)
00 Mem(3)
Start with an empty cache - all blocks initially marked as not valid
  8 requests, 6 misses
0000 0001 0010 0011 0100 0011 0100 1111
Notes: For lecture
Reference string is word addresses (or block number since we are using one word blocks) – i.e., the low order two bits used to selected the byte in the 32-bit word are ignored

## Slide 13: Multiword Block Direct Mapped Cache
Four words/block, cache size = 1K words
8
Index
Data
Index
Tag
Valid
0
1
2
.
.
.
253
254
255
31 30 . . . 13 12 11 . . . 4 3 2 1 0
Byte offset
20
20
Tag
Hit
Data
32
Block offset
What kind of locality are we taking advantage of?
Notes: to take advantage for spatial locality want a cache block that is larger than word word in size.

## Slide 14: Taking Advantage of Spatial Locality
0
Let cache block hold more than one word
  0 1 2 3 4 3 4 15
1
2
3
4
3
4
15
00 Mem(1) Mem(0)
miss
00 Mem(1) Mem(0)
hit
00 Mem(3) Mem(2)
00 Mem(1) Mem(0)
miss
hit
00 Mem(3) Mem(2)
00 Mem(1) Mem(0)
miss
00 Mem(3) Mem(2)
00 Mem(1) Mem(0)
01
5
4
hit
00 Mem(3) Mem(2)
01 Mem(5) Mem(4)
hit
00 Mem(3) Mem(2)
01 Mem(5) Mem(4)
00 Mem(3) Mem(2)
01 Mem(5) Mem(4)
miss
11
15
14
Start with an empty cache - all blocks initially marked as not valid
  8 requests, 4 misses
Notes: For lecture
Show the 4-bit address mapping – 2-bits of tag, 1-bit of set address (index), 1-bit of word-in-block select

## Slide 15: Miss Rate vs Block Size vs Cache Size
Chart: Block size (bytes)
| 16 | 32 | 64 | 128 | 256
8 KB | 8.5 | 7.5 | 7.25 | 7.75 | 9.5
16 KB | 4 | 2.75 | 2.75 | 3 | 3.5
64 KB | 2 | 1.7 | 1.55 | 1.4 | 1.4
256 KB | 1 | 0.7 | 0.5 | 0.5 | 0.6
Miss rate goes up if the block size becomes a significant fraction of the cache size because the number of blocks that can be held in the same size cache is smaller (increasing capacity misses)
Notes: Increasing the block size usually decreases the miss rate.
A more serious problem is that the miss penalty goes up since it is primarily determined by the time to fetch the block from the next lower level of the hierarchy and load it into the cache.

## Slide 16: Average Memory Access Time (AMAT)
Average Memory Access Time (AMAT) is the average to access memory considering both hits and misses
  AMAT = Time for a hit + Miss rate x Miss penalty
What is the AMAT for a processor with a 200 psec clock, a miss penalty of 50 clock cycles, a miss rate of 0.02 misses per instruction and a cache access time of 1 clock cycle?
Potential impact of much larger cache on AMAT?
1 + 0.02 x 50 = 2 clock cycles
Or 2 x 200 = 400 psecs
1) Lower Miss rate
2) Longer Access time (Hit time): smaller is faster
At some point, increase in hit time for a larger cache may overcome the improvement in hit rate, yielding a decrease in performance
Notes: AMAT = 1 + 0.02x50 = 2

## Slide 17: Block Size Tradeoff (1/3)
Benefits of Larger Block Size
  Spatial Locality: if we access a given word, we’re likely to access other nearby words soon
  Very applicable with Stored-Program Concept: if we execute a given instruction, it’s likely that we’ll execute the next few as well
  Works nicely in sequential array accesses too
Notes: As I said earlier, block size is a tradeoff. In general, larger block size will reduce the miss rate because it take advantage of spatial locality.
But remember, miss rate NOT the only cache performance metrics. You also have to worry about miss penalty.
As you increase the block size, your miss penalty will go up because as the block gets larger, it will take you longer to fill up the block.
Even if you look at miss rate by itself, which you should NOT, bigger block size does not always win. As you increase the block size, assuming keeping cache size constant, your miss rate will drop off rapidly at the beginning due to spatial locality.
However, once you pass certain point, your miss rate actually goes up.
As a result of these two curves, the Average Access Time (point to equation), which is really the more important performance metric than the miss rate, will go down initially because the miss rate is dropping much faster than the increase in miss penalty.
But eventually, as you keep on increasing the block size, the average access time can go up rapidly because not only is the miss penalty is increasing, the miss rate is increasing as well.
Let me show you why your miss rate may go up as you increase the block size by another extreme example.
+3 = 33 min. (Y:13)

## Slide 18: Block Size Tradeoff (2/3)
Drawbacks of Larger Block Size
  Larger block size means larger miss penalty
    on a miss, takes longer time to load a new block from next level
  If block size is too big relative to cache size, then there are too few blocks
    Result: miss rate goes up
In general, minimize Average Memory Access Time (AMAT)
  = Hit Time + Miss Penalty x Miss Rate

## Slide 19: Block Size Tradeoff (3/3)
Hit Time
  time to find and retrieve data from current level cache
Miss Penalty
  average time to retrieve data on a current level miss (includes the possibility of misses on successive levels of memory hierarchy)
Hit Rate
  % of requests that are found in current level cache
Miss Rate
  1 - Hit Rate

## Slide 20: Extreme Example: One Big Block
Cache Size = 4 bytes Block Size = 4 bytes
  Only ONE entry (row) in the cache!
If item accessed, likely accessed again soon
  But unlikely will be accessed again immediately!
The next access will likely to be a miss again
  Continually loading data into the cache but discard data (force out) before use it again
  Nightmare for cache designer: Ping Pong Effect
Cache Data
Valid Bit
B 0
B 1
B 3
Tag
B 2

## Slide 21: Block Size Tradeoff Conclusions
Miss
Penalty
Block Size
Increased Miss Penalty
& Miss Rate
Average
Access
Time
Block Size
Exploits Spatial Locality
Fewer blocks:
compromises
temporal locality
Miss
Rate
Block Size

## Slide 22: What to do on a write hit?
Write-through
  update the word in cache block and corresponding word in memory
Write-back
  update word in cache block
  allow memory word to be “stale”
  add ‘dirty’ bit to each block indicating that memory needs to be updated when block is replaced
  OS flushes cache before I/O…
Performance trade-offs?

## Slide 23: Types of Cache Misses (1/2)
“Three Cs” Model of Misses
1st C: Compulsory Misses
  occur when a program is first started
  cache does not contain any of that program’s data yet, so misses are bound to occur
  can’t be avoided easily, so won’t focus on these in this course

## Slide 24: Types of Cache Misses (2/2)
2nd C: Conflict Misses
  miss that occurs because two distinct memory addresses map to the same cache location
  two blocks (which happen to map to the same location) can keep overwriting each other
  big problem in direct-mapped caches
  how do we lessen the effect of these?
Dealing with Conflict Misses
  Solution 1: Make the cache size bigger
    Fails at some point
  Solution 2: Multiple distinct blocks can fit in the same cache Index
    How???

## Slide 25: Fully Associative Cache (1/3)
Memory address fields:
  Tag: same as before
  Offset: same as before
  Index: non-existant
What does this mean?
  no “rows”: any block can go anywhere in the cache
  must compare with all tags in entire cache to see if data is there

## Slide 26: Fully Associative Cache (2/3)
Fully Associative Cache (e.g., 32 B block)
  compare tags in parallel
Byte Offset
:
Cache Data
B 0
0
4
31
:
Cache Tag (27 bits long)
Valid
:
B 1
B 31
:
Cache Tag
=
=
=
=
=
:

## Slide 27: Fully Associative Cache (3/3)
Benefit of Fully Assoc. Cache
  No Conflict Misses (since data can go anywhere)
Drawbacks of Fully Assoc. Cache
  Need hardware comparator for every single entry: if we have a 64KB of data in cache with 4B entries, we need 16K comparators: infeasibly high cost

## Slide 28: Final Type of Cache Miss
3rd C: Capacity Misses
  miss that occurs because the cache has a limited size
  miss that would not occur if we increase the size of the cache
  sketchy definition, so just get the general idea
This is the primary type of miss for Fully Associative caches.

## Slide 29: N-Way Set Associative Cache (1/3)
Memory address fields:
  Tag: same as before
  Offset: same as before
  Index: points us to the correct “row” (called a set in this case)
So what’s the difference?
  each set contains multiple blocks
  once we’ve found correct set, must compare with all tags in that set to find our data
  Hybrid of direct-mapped and fully associative

## Slide 30: Associative Cache Example
Here’s a simple 2-way set associative cache.
Memory
Memory Address
0
1
2
3
4
5
6
7
8
9
A
B
C
D
E
F
Cache
Index
0
1
Notes: Let’s look at the simplest cache one can build. A direct mapped cache that only has 4 bytes.
In this direct mapped cache with only 4 bytes, location 0 of the cache can be occupied by data form memory location 0, 4, 8, C, ... and so on.
While location 1 of the cache can be occupied by data from memory location 1, 5, 9, ... etc.
So in general, the cache location where a memory location can map to is uniquely determined by the 2 least significant bits of the address (Cache Index).
For example here, any memory location whose two least significant bits of the address are 0s can go to cache location zero.
With so many memory locations to chose from, which one should we place in the cache?
Of course, the one we have read or write most recently because by the principle of temporal locality, the one we just touch is most likely to be the one we will need again soon.
Of all the possible memory locations that can be placed in cache Location 0, how can we tell which one is in the cache?
+2 = 22 min. (Y:02)

## Slide 31: N-Way Set Associative Cache (2/3)
Basic Idea
  cache is direct-mapped w/respect to sets
  each set is fully associative with N blocks in it
Given memory address:
  Find correct set using Index value.
  Compare Tag with all Tag values in the determined set.
  If a match occurs, hit!, otherwise a miss.
  Finally, use the offset field as usual to find the desired data within the block.

## Slide 32: N-Way Set Associative Cache (3/3)
What’s so great about this?
  even a 2-way set assoc. cache avoids a lot of conflict misses
  hardware cost isn’t that bad: only need N comparators
In fact, for a cache with M blocks,
  it’s Direct-Mapped if it’s 1-way set assoc.
  it’s Fully Assoc if it’s M-way set assoc.
  so these two are just special cases of the more general set associative design

## Slide 33: 4-Way Set Associative Cache Circuit

## Slide 34: Summary
Principle of Locality for Computer Memory
Hierarchy of Memories (speed/size/cost per bit) to Exploit Locality
Cache – copy of data lower level in memory hierarchy
Direct Mapped to find block in cache using Tag field and Valid bit for Hit
Larger caches reduce Miss rate via Temporal and Spatial Locality, but can increase Hit time
Larger blocks to reduces Miss rate via Spatial Locality, but increase Miss penalty
AMAT helps balance Hit time, Miss rate, Miss penalty