## Slide 1: CSE 31 Computer Organization
Lecture 22 – CPU Design (1)

## Slide 2: Announcement
No lab this week
  Project #1 grading during lab
HW #6 out at CatCourses (not zyBooks)
  Due Friday (11/30, extended) at 11:59pm
Project #2
  Due Monday (12/3)
    Don’t start late, you won’t have time!
Course evaluation online
  Fill out by 12/6 (Thursday)
Reading assignment
  Chapter 5.1 – 5.6 of zyBooks (Reading Assignment #6)
    Make sure to do the Participation Activities
    Due Monday (11/26)

## Slide 3: Announcement
Midterm Exam 2
  11/28 (Wednesday, in lecture) Not 11/7 as scheduled
  Lectures #8 - #18
  HW #3 - #5
  Practice exam in CatCourses
  Closed book
  1 sheet of note (8.5” x 11”)
  MIPS reference sheet will be provided

## Slide 4: Review
C program: foo.c
Assembly program: foo.s
Executable(mach lang pgm): a.out
Compiler
Assembler
Linker
Loader
Memory
Object(mach lang module): foo.o
lib.o

## Slide 5: What are “Machine Structures”?
CSE 31
Coordination of many levels of abstraction
I/O system
Processor
Compiler
Operating
System
(MacOS X)
Application (Chrome)
Digital Design
Circuit Design
Instruction Set
Architecture
Datapath & Control
transistors
Memory
Hardware
Software
Assembler
ISA is an important abstraction level: contract between HW & SW

## Slide 6: Below the Program
High-level language program (in C)
  swap int v[], int k){
  int temp;
  temp = v[k];
  v[k] = v[k+1];
  v[k+1] = temp;
  }
Assembly language program (for MIPS)
  swap: sll $2, $5, 2
  add $2, $4,$2
  lw $15, 0($2)
  lw $16, 4($2)
  sw $16, 0($2)
  sw $15, 4($2)
  jr $31
Machine (object) code (for MIPS)
  000000 00000 00101 0001000010000000
  000000 00100 00010 0001000000100000 . . .
C compiler
assembler
?
Notes: For lecture
Computer only understands zeros and ones – instructions of 0’s and 1’s
Early programmers found representing machine instructions in a symbolic notation – assembly language
And developed programs that translate from assembler to machine code
Eventually, programmers found working even in assembler too tedious so migrated to higher-level languages and developed compilers that would translate from the higher-level languages to assembler

## Slide 7: Synchronous Digital Systems
Synchronous:
  Means all operations are coordinated by a central clock.
    It keeps the “heartbeat” of the system!
The hardware of a processor, such as the MIPS, is an example of a Synchronous Digital System
Digital:
  Mean all values are represented by discrete values
  Electrical signals are treated as 1’s and 0’s and grouped together to form words.

## Slide 8: PowerPC Die Photograph
Let’s look closer…

## Slide 9: Transistors 101
MOSFET
  Metal-Oxide-Semiconductor Field-Effect Transistor
  Come in two types:
    n-type NMOSFET
    p-type PMOSFET
For n-type (p-type opposite)
  If voltage not enough between G & S, transistor turns “off” (cut-off) and Drain-Source NOT connected
  If the G & S voltage is high enough, transistor turns “on” (saturation) and Drain-Source ARE connected
p-type
n-type
D
G
S
S
G
D
Side view
www.wikipedia.org/wiki/Mosfet

## Slide 10: Transistor Circuit Rep. vs. Block diagram
Chips is composed of nothing but transistors and wires.
Small groups of transistors form useful building blocks.
Block are organized in a hierarchy to build higher-level blocks: ex: adders.
a
b
c
0
0
1
0
1
1
1
0
1
1
1
0
“1” (voltage source)
“0” (ground)

## Slide 11: Five Components of a Computer
Processor
Computer
Control
Datapath
Memory
(passive)
(where
programs,
data live
when
running)
Devices
Input
Output
Keyboard, Mouse
Display, Printer
Disk (where
programs,
data live when not running)

## Slide 12: The CPU
Processor (CPU): the active part of the computer, which does all the work (data manipulation and decision-making)
Datapath: portion of the processor which contains hardware necessary to perform operations required by the processor (the brawn)
Control: portion of the processor (also in hardware) which tells the datapath what needs to be done (the brain)

## Slide 13: Stages of the Datapath
Problem: a single, atomic block which “executes an instruction” (performs all necessary operations beginning with fetching the instruction) would be too bulky and inefficient
Solution: break up the process of “executing an instruction” into stages, and then connect the stages to create the whole datapath
  smaller stages are easier to design
  easy to optimize (change) one stage without touching the others

## Slide 14: Stages of the Datapath (1/5)
There is a wide variety of MIPS instructions: so what general steps do they have in common?
Stage 1: Instruction Fetch
  no matter what the instruction type is, the 32-bit instruction word must first be fetched from memory (the cache-memory hierarchy)
  also, this is where we Increment PC (that is, PC = PC + 4, to point to the next instruction: byte addressing so + 4)

## Slide 15: Stages of the Datapath (2/5)
Stage 2: Instruction Decode
  upon fetching the instruction, we next gather data from the fields (decode all necessary instruction data)
  first, read the opcode to determine instruction type and field lengths
  second, read in data from all necessary registers
    for add, read two registers (R-format)
    for addi, read one register (I-format)
    for jal, no reads necessary (J-format)

## Slide 16: Stages of the Datapath (3/5)
Stage 3: ALU (Arithmetic-Logic Unit)
  the real work of most instructions is done here: arithmetic (+, -, *, /), shifting, logic (&, |), comparisons (slt)
  what about loads and stores, do they need this stage?
    lw $t0, 40($t1)
    the address we are accessing in memory = the value in $t1 PLUS the value 40
    so we do this addition in this stage

## Slide 17: Stages of the Datapath (4/5)
Stage 4: Memory Access
  actually only the load and store instructions do anything during this stage; the others remain idle during this stage or skip it all together
  since these instructions have a unique step, we need this extra stage to account for them
  as a result of the cache system, this stage is expected to be fast

## Slide 18: Stages of the Datapath (5/5)
Stage 5: Register Write
  most instructions write the result of some computation into a register
  examples: arithmetic, logical, shifts, loads, slt
  what about stores, branches, jumps?
    don’t write anything into a register at the end
    these remain idle during this fifth stage or skip it all together

## Slide 19: Generic Diagram of Datapath
instruction
memory
+4
rt
rs
rd
registers
ALU
Data
memory
imm
1. Instruction
Fetch
2. Decode/
Register
Read
3. Execute
4. Memory
5. Register
Write
PC

## Slide 20: Datapath Walkthroughs (1/3)
add $r3,$r1,$r2 # r3 = r1+r2
  Stage 1: fetch this instruction, inc. PC
  Stage 2: decode to find it’s an add, then read registers $r1 and $r2
  Stage 3: add the two values retrieved in Stage 2
  Stage 4: idle (nothing to write to memory)
  Stage 5: write result of Stage 3 into register $r3

## Slide 21: Example: add Instruction
instruction
memory
+4
registers
ALU
Data
memory
imm
2
1
3
add r3, r1, r2
reg[1]+ reg[2]
reg[2]
reg[1]
PC

## Slide 22: Datapath Walkthroughs (2/3)
slti $r3,$r1,17
  Stage 1: fetch this instruction, inc. PC
  Stage 2: decode to find it’s an slti, then read register $r1
  Stage 3: compare value retrieved in Stage 2 with the integer 17
  Stage 4: idle
  Stage 5: write the result of Stage 3 in register $r3

## Slide 23: Example: slti Instruction
instruction
memory
+4
registers
ALU
Data
memory
imm
3
1
x
slti r3, r1, 17
reg[1] <17?
17
reg[1]
PC

## Slide 24: Datapath Walkthroughs (3/3)
sw $r3, 17($r1)
  Stage 1: fetch this instruction, inc. PC
  Stage 2: decode to find it’s a sw, then read registers $r1 and $r3
  Stage 3: add 17 to value in register $r1 (retrieved in Stage 2)
  Stage 4: write value in register $r3 (retrieved in Stage 2) into memory address computed in Stage 3
  Stage 5: idle (nothing to write into a register)

## Slide 25: Example: sw Instruction
instruction
memory
+4
registers
ALU
Data
memory
imm
3
1
x
SW r3, 17(r1)
reg[1] +17
17
reg[1]
MEM[r1+17]<=r3
reg[3]
PC

## Slide 26: Why Five Stages? (1/2)
Could we have a different number of stages?
  Yes, and other architectures do
So why does MIPS have five if instructions tend to idle for at least one stage?
  The five stages are the union of all the operations needed by all the instructions.
  There is one instruction that uses all five stages: the load

## Slide 27: Why Five Stages? (2/2)
lw $r3, 17($r1)
  Stage 1: fetch this instruction, inc. PC
  Stage 2: decode to find it’s a lw, then read register $r1
  Stage 3: add 17 to value in register $r1 (retrieved in Stage 2)
  Stage 4: read value from memory address compute in Stage 3
  Stage 5: write value found in Stage 4 into register $r3

## Slide 28: Example: lw Instruction
ALU
instruction
memory
+4
registers
Data
memory
imm
3
1
x
LW r3, 17(r1)
reg[1] +17
17
reg[1]
MEM[r1+17]
PC

## Slide 29: Datapath Summary
Datapath based on data transfers required to perform instructions
Controller causes the right transfers to happen
PC
instruction
memory
+4
rt
rs
rd
registers
Data
memory
imm
ALU
Controller
opcode, funct

## Slide 30: CPU clocking (1/2)
For each instruction, how do we control the flow of information though the datapath?
Single Cycle CPU: All stages of an instruction completed within one long clock cycle
  Clock cycle sufficiently long to allow each instruction to complete all stages without interruption within one cycle
1. Instruction
Fetch
2. Decode/
Register
Read
3. Execute
4. Memory
5. Reg.
Write

## Slide 31: CPU clocking (2/2)
Multiple-cycle CPU: only one stage of instruction per clock cycle
  Clock is made as long as the slowest stage
  Several significant advantages over single cycle execution: Unused stages in a particular instruction can be skipped OR instructions can be pipelined (overlapped)
  Will talk about this in CSE 140!
1. Instruction
Fetch
2. Decode/
Register
Read
3. Execute
4. Memory
5. Register
Write

## Slide 32: What Hardware Is Needed? (1/2)
PC: a register which keeps track of memory addr of the next instruction
General Purpose Registers
  used in Stages 2 (Read) and 5 (Write)
  MIPS has 32 of these
Memory
  used in Stages 1 (Fetch) and 4 (R/W)
  cache system makes these two stages as fast as the others, on average

## Slide 33: What Hardware Is Needed? (2/2)
ALU
  used in Stage 3
  something that performs all necessary functions: arithmetic, logicals, etc.
  we’ll design details later
Miscellaneous Registers
  In implementations with only one stage per clock cycle, registers are inserted between stages to hold intermediate data and control signals as they travels from stage to stage.
  Note: Register is a general purpose term meaning something that stores bits. Not all registers are in the “register file”.

## Slide 34: Quiz
If the destination reg is the same as the source reg, we could compute the incorrect value!
We’re going to be able to read 2 registers and write a 3rd in 1 cycle
Datapath is hard, Control is easy

## Slide 35: Summary
CPU design involves Datapath,Control
  Datapath in MIPS involves 5 CPU stages
    Instruction Fetch
    Instruction Decode & Register Read
    ALU (Execute)
    Memory
    Register Write