## Slide 1: CSE 31 Computer Organization
Lecture 23 – CPU Design (2)

## Slide 2: Announcement
No lab this week
  Project #1 grading during lab
HW #7 at zyBooks
  Due Monday(12/10) at 11:59pm
Project #2
  Due Monday (12/3)
    Don’t start late, you won’t have time!
Course evaluation online
  Fill out by 12/6 (Thursday)
Reading assignment
  Chapter 5.7 – 5.11 of zyBooks (Reading Assignment #6)
    Make sure to do the Participation Activities
    Due Wednesday (12/5)

## Slide 3: Announcement
Final Exam
  12/11 (Tuesday), 11:30 – 2:30pm
  Cover all
  Practice exam in CatCourses
  Closed book
  2 sheet of note (8.5” x 11”)
  MIPS reference sheet will be provided
  Review: 12/10 (Monday) 1-3pm, COB 113

## Slide 4: Review
CPU design involves Datapath,Control
  Datapath in MIPS involves 5 CPU stages
    Instruction Fetch
    Instruction Decode & Register Read
    ALU (Execute)
    Memory
    Register Write

## Slide 5: Generic Steps of Datapath
instruction
memory
+4
rt
rs
rd
registers
ALU
Data
memory
imm
1. Instruction
Fetch
2. Decode/
Register
Read
3. Execute
4. Memory
5. Register
Write
PC
How do we handle the different register usage between r-type and i-type instructions?

## Slide 6: Data Multiplexor (mux) (2-to-1, n-bits)
“mux”

## Slide 7: 4-to-1 Multiplexor?

## Slide 8: A zoomed in version of RegFile and ALU
32
ALUctr
clk
RegWr
32
32
busA
32
busB
5
5
Rw
Ra
Rb
RegFile
Rs
Rt
Rt
Rd
Extender
32
16
imm16
ALUSrc
0
1
0
1
ALU
5
RegDst
  To choose which register to store the result
To choose which input to ALU
To extend 16 bits into 32 bits

## Slide 9: Operations with Immediate
R[rt] = R[rs] op ZeroExt[imm16] ]
op
rs
rt
immediate
0
16
21
26
31
6 bits
16 bits
5 bits
5 bits
immediate
0
16
15
31
16 bits
16 bits
0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0
32
ALUctr
clk
RegWr
32
32
busA
32
busB
5
5
Rw
Ra
Rb
RegFile
Rs
Rt
Rt
Rd
ZeroExt
32
16
imm16
ALUSrc
0
1
0
1
ALU
5
RegDst
Notes: Here is the datapath for the Or immediate instructions.
We cannot use the Rd field here (Rw) because in this instruction format, we don’t have a Rd field. The Rd field in the R-type is used here as part of the immediate field.
For this instruction type, Rw input of the register file, that is the address of the register to be written, comes from the Rt field of the instruction.
Recalled from earlier slide that for R-type instruction, the Rw comes from the Rd field.
That’s why we need a MUX here to put Rd onto Rw for R-type instructions and to put Rt onto Rw for the I-type instruction.
Since the second operation of this instruction will be the immediate field zero extended to 32 bits, we also need a MUX here to block off bus B from the register file.
Since bus B is blocked off by the MUX, the value on bus B is don’t care. Therefore we do not have to worry about what ends up on the register file’s Rb register specifier.
To keep things simple, we may just as well keep it the same as the R-type instruction and put the Rt field here.
So to summarize, this is how this datapath works. With Rs on Register File’s Ra input, bus A will get the value of Rs as the first ALU operand.
The second operand will come from the immediate field of the instruction.
Once the ALU complete the OR operation, the result will be written into the register specified by the instruction’s Rt field.
+3 = 50 min. (Y:30)

## Slide 10: Operations with Immediate
R[rt] = R[rs] op ZeroExt[imm16] ]
op
rs
rt
immediate
0
16
21
26
31
6 bits
16 bits
5 bits
5 bits
immediate
0
16
15
31
16 bits
16 bits
0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0
What about Rt register read (bus B)??
32
ALUctr
clk
RegWr
32
32
busA
32
busB
5
5
Rw
Ra
Rb
RegFile
Rs
Rt
Rt
Rd
ZeroExt
32
16
imm16
ALUSrc
0
1
0
1
ALU
5
RegDst
We don’t care!
Why?
Bus B is blocked
Notes: Here is the datapath for the Or immediate instructions.
We cannot use the Rd field here (Rw) because in this instruction format, we don’t have a Rd field. The Rd field in the R-type is used here as part of the immediate field.
For this instruction type, Rw input of the register file, that is the address of the register to be written, comes from the Rt field of the instruction.
Recalled from earlier slide that for R-type instruction, the Rw comes from the Rd field.
That’s why we need a MUX here to put Rd onto Rw for R-type instructions and to put Rt onto Rw for the I-type instruction.
Since the second operation of this instruction will be the immediate field zero extended to 32 bits, we also need a MUX here to block off bus B from the register file.
Since bus B is blocked off by the MUX, the value on bus B is don’t care. Therefore we do not have to worry about what ends up on the register file’s Rb register specifier.
To keep things simple, we may just as well keep it the same as the R-type instruction and put the Rt field here.
So to summarize, this is how this datapath works. With Rs on Register File’s Ra input, bus A will get the value of Rs as the first ALU operand.
The second operand will come from the immediate field of the instruction.
Once the ALU complete the OR operation, the result will be written into the register specified by the instruction’s Rt field.
+3 = 50 min. (Y:30)

## Slide 11: Load Memory
R[rt] = Mem[R[rs] + SignExt[imm16]]
Example: lw rt,rs,imm16
op
rs
rt
immediate
0
16
21
26
31
6 bits
16 bits
5 bits
5 bits
32
ALUctr
clk
RegWr
32
32
busA
32
busB
5
5
Rw
Ra
Rb
RegFile
Rs
Rt
Rt
Rd
SignExt
32
16
imm16
ALUSrc
0
1
0
1
ALU
5
RegDst
Do we store the result of ALU?
What is the result of ALU for?
We need to add a memory unit!
Notes: Once again we cannot use the instruction’s Rd field for the Register File’s Rw input because load is a I-type instruction and there is no such thing as the Rd field in the I format.
So instead of Rd, the Rt field is used to specify the destination register through this two to one multiplexor.
The first operand of the ALU comes from busA of the register file which contains the value of Register Rs (points to the Ra input of the register file).
The second operand, on the other hand, comes from the immediate field of the instruction.
Instead of using the Zero Extender I used in datapath for the or immediate datapath, I have to use a more general purpose Extender that can do both Sign Extend and Zero Extend.
The ALU then adds these two operands together to form the memory address.
Consequently, the output of the ALU has to go to two places:
(a) First the address input of the data memory.
(b) And secondly, also to the input of this two-to-one multiplexer.
The other input of this multiplexer comes from the output of the data memory so we can place the output of the data memory onto the register file’s input bus for the load instruction.
For Add, Subtract, and the Or immediate instructions, the output of the ALU will be selected to be placed on the input bus of the register file.
In either case, the control signal RegWr should be asserted so the register file will be written at the end of the cycle.
+3 = 60 min. (Y:40)

## Slide 12: Load Memory
R[rt] = Mem[R[rs] + SignExt[imm16]]
Example: lw rt,rs,imm16
op
rs
rt
immediate
0
16
21
26
31
6 bits
16 bits
5 bits
5 bits
32
ALUctr
clk
busW
RegWr
32
32
busA
32
busB
5
5
Rw
Ra
Rb
RegFile
Rs
Rt
Rt
Rd
RegDst
Extender
32
16
imm16
ALUSrc
ExtOp
MemtoReg
clk
Data In
32
MemWr
0
1
0
1
ALU
0
1
WrEn
Adr
Data
Memory
5
?
Notes: Once again we cannot use the instruction’s Rd field for the Register File’s Rw input because load is a I-type instruction and there is no such thing as the Rd field in the I format.
So instead of Rd, the Rt field is used to specify the destination register through this two to one multiplexor.
The first operand of the ALU comes from busA of the register file which contains the value of Register Rs (points to the Ra input of the register file).
The second operand, on the other hand, comes from the immediate field of the instruction.
Instead of using the Zero Extender I used in datapath for the or immediate datapath, I have to use a more general purpose Extender that can do both Sign Extend and Zero Extend.
The ALU then adds these two operands together to form the memory address.
Consequently, the output of the ALU has to go to two places:
(a) First the address input of the data memory.
(b) And secondly, also to the input of this two-to-one multiplexer.
The other input of this multiplexer comes from the output of the data memory so we can place the output of the data memory onto the register file’s input bus for the load instruction.
For Add, Subtract, and the Or immediate instructions, the output of the ALU will be selected to be placed on the input bus of the register file.
In either case, the control signal RegWr should be asserted so the register file will be written at the end of the cycle.
+3 = 60 min. (Y:40)

## Slide 13: Store Memory
Mem[ R[rs] + SignExt[imm16] ] = R[rt] Ex.: sw rt, rs, imm16
op
rs
rt
immediate
0
16
21
26
31
6 bits
16 bits
5 bits
5 bits
32
ALUctr
clk
busW
RegWr
32
32
busA
32
busB
5
5
Rw
Ra
Rb
RegFile
Rs
Rt
Rt
Rd
RegDst
Extender
32
16
imm16
ALUSrc
ExtOp
MemtoReg
clk
Data In
32
MemWr
0
1
0
1
ALU
0
1
WrEn
Adr
Data
Memory
5
Notes: And here is the datapath for the store instruction.
The Register File, the ALU, and the Extender are the same as the datapath for the load instruction because the memory address has to be calculated the same exact way:
(a) Put the register selected by Rs onto bus A and sign extend the 16 bit immediate field.
(b) Then make the ALU (ALUctr) adds these two (busA and output of Extender) together.
The new thing we added here is busB extension (DataIn).
More specifically, in order to send the register selected by the Rt field (Rb of the register file) to data memory, we need to connect bus B to the data memory’s Data In bus.
Finally, the store instruction is the first instruction we encountered that does not do any register write at the end.
Therefore the control unit must make sure RegWr is zero for this instruction.
+2 = 64 min. (Y:44)

## Slide 14: Store Memory
op
rs
rt
immediate
0
16
21
26
31
6 bits
16 bits
5 bits
5 bits
32
ALUctr
clk
busW
RegWr
32
32
busA
32
busB
5
5
Rw
Ra
Rb
RegFile
Rs
Rt
Rt
Rd
RegDst
Extender
32
16
imm16
ALUSrc
ExtOp
MemtoReg
clk
Data In
32
MemWr
0
1
0
1
ALU
0
1
WrEn
Adr
Data
Memory
5
Mem[ R[rs] + SignExt[imm16] ] = R[rt] Ex.: sw rt, rs, imm16
Notes: And here is the datapath for the store instruction.
The Register File, the ALU, and the Extender are the same as the datapath for the load instruction because the memory address has to be calculated the same exact way:
(a) Put the register selected by Rs onto bus A and sign extend the 16 bit immediate field.
(b) Then make the ALU (ALUctr) adds these two (busA and output of Extender) together.
The new thing we added here is busB extension (DataIn).
More specifically, in order to send the register selected by the Rt field (Rb of the register file) to data memory, we need to connect bus B to the data memory’s Data In bus.
Finally, the store instruction is the first instruction we encountered that does not do any register write at the end.
Therefore the control unit must make sure RegWr is zero for this instruction.
+2 = 64 min. (Y:44)

## Slide 15: Datapath for Branch Operations
beq rs, rt, imm16 Datapath generates condition (equal)
op
rs
rt
immediate
0
16
21
26
31
6 bits
16 bits
5 bits
5 bits
Already have mux, adder, need special sign need equal compare (sub?), update for PC,
imm16
clk
PC
00
4
nPC_sel
PC Ext
Adder
Adder
Mux
Inst Address
32
ALUctr
clk
busW
RegWr
32
busA
32
busB
5
5
Rw
Ra
Rb
RegFile
Rs
Rt
ALU
5
=
Equal
Notes: The datapath for calculating the branch condition is rather simple.
All we have to do is feed the Rs and Rt fields of the instruction into the Ra and Rb inputs of the register file.
Bus A will then contain the value from the register selected by Rs.
And bus B will contain the value from the register selected by Rt.
The next thing to do is to ask the ALU to perform a subtract operation and feed the output Zero to the next address logic.
How does the next address logic block look like?
Well, before I show you that, let’s take a look at the binary arithmetics behind the program counter (PC).
+2 = 67 min. (Y:47)

## Slide 16: Single Cycle Datapath
imm16
32
ALUctr
clk
busW
RegWr
32
32
busA
32
busB
5
5
Rw
Ra
Rb
RegFile
Rs
Rt
Rt
Rd
RegDst
Extender
32
16
imm16
ALUSrc
ExtOp
MemtoReg
clk
Data In
32
MemWr
Equal
Instruction<31:0>
<21:25>
<16:20>
<11:15>
<0:15>
Imm16
Rd
Rt
Rs
clk
PC
00
4
nPC_sel
PC Ext
Adr
Inst
Memory
Adder
Adder
Mux
0
1
0
1
=
ALU
0
1
WrEn
Adr
Data
Memory
5
Notes: So here is the single cycle datapath we just built.
If you push into the Instruction Fetch Unit, you will see the last slide showing the PC, the next address logic, and the Instruction Memory.
Here I have shown how we can get the Rt, Rs, Rd, and Imm16 fields out of the 32-bit instruction word.
The Rt, Rs, and Rd fields will go to the register file as register specifiers while the Imm16 field will go to the Extender where it is either Zero and Sign extended to 32 bits.
The signals ExtOp, ALUSrc, ALUctr, MemWr, MemtoReg, RegDst, RegWr, Branch, and Jump are control signals.
And I will show you how to generate them on Friday.
+2 = 80 min. (Z:00)

## Slide 17: Abstract View of the Implementation
Data
Out
clk
5
Rw
Ra
Rb
Register
File
Rd
Data In
Data
Addr
Ideal
Data
Memory
Instruction
Instruction
Address
Ideal
Instruction
Memory
PC
5
Rs
5
Rt
32
32
32
32
A
B
Next Address
Control
Datapath
Control Signals
Conditions
clk
clk
ALU
Notes: One thing you may noticed from our last slide is that almost all instructions, except Jump, require reading some registers, do some computation, and then do something else.
Therefore our datapath will look something like this.
For example, if we have an add instruction (points to the output of Instruction Memory), we will read the registers from the register file (Ra, Rb and then busA and busB).
Add the two numbers together (ALU) and then write the result back to the register file.
On the other hand, if we have a load instruction, we will first use the ALU to calculate the memory address.
Once the address is ready, we will use it to access the Data Memory.
And once the data is available on Data Memory’s output bus, we will write the data to the register file. Well, this is simple enough.
But if it is this simple, you probably won’t need to take this class.
So in today’s lecture, I will show you how to turn this abstract datapath into a real datapath by making it slightly (JUST slightly) more complicated so it can do real work for you.
But before we do that, let’s do a quick review of the clocking methodology
+3 = 16 (X:56)

## Slide 18: A Single Cycle Datapath
32
ALUctr
clk
busW
RegWr
32
32
busA
32
busB
5
5
Rw
Ra
Rb
RegFile
Rs
Rt
Rt
Rd
RegDst
Extender
32
16
imm16
ALUSrc
ExtOp
MemtoReg
clk
Data In
32
MemWr
zero
0
1
0
1
=
ALU
0
1
WrEn
Adr
Data
Memory
5
Instruction<31:0>
<21:25>
<16:20>
<11:15>
<0:15>
Imm16
Rd
Rt
Rs
nPC_sel
instr
fetch
unit
clk
We have everything except control signals
Notes: The result of the last lecture is this single-cycle datapath.
+1 = 6 min. (X:46)

## Slide 19: Meaning of the Control Signals
nPC_sel: “+4”: 0 ⇒ PC <– PC + 4 “br”: 1 ⇒ PC <– PC + 4 + {SignExt(Im16) , 00 }
Later in lecture: higher-level connection between mux and branch condition
“n”=next
imm16
clk
PC
00
4
nPC_sel
PC Ext
Adder
Adder
Mux
Inst Address
0
1

## Slide 20: Meaning of the Control Signals
ExtOp: “zero”, “sign”
ALUsrc: 0 ⇒ regB; 1 ⇒ immed
ALUctr: “ADD”, “SUB”, “OR”
MemWr: 1 ⇒ write memory
MemtoReg: 0 ⇒ ALU; 1 ⇒ Mem
RegDst: 0 ⇒ “rt”; 1 ⇒ “rd”
RegWr: 1 ⇒ write register
32
ALUctr
clk
busW
RegWr
32
32
busA
32
busB
5
5
Rw
Ra
Rb
RegFile
Rs
Rt
Rt
Rd
RegDst
Extender
32
16
imm16
ALUSrc
ExtOp
MemtoReg
clk
Data In
32
MemWr
0
1
0
1
ALU
0
1
WrEn
Adr
Data
Memory
5

## Slide 21: The Add Instruction
add rd, rs, rt
  MEM[PC] Fetch the instruction from memory
  R[rd] = R[rs] + R[rt] The actual operation
  PC = PC + 4 Calculate the next instruction’s address
op
rs
rt
rd
shamt
funct
0
6
11
16
21
26
31
6 bits
6 bits
5 bits
5 bits
5 bits
5 bits
Notes: OK, let’s get on with today’s lecture by looking at the simple add instruction.
In terms of Register Transfer Language, this is what the Add instruction need to do.
First, you need to fetch the instruction from Memory.
Then you perform the actual add operation. More specifically:
(a) You add the contents of the register specified by the Rs and Rt fields of the instruction.
(b) Then you write the results to the register specified by the Rd field.
And finally, you need to update the program counter to point to the next instruction.
Now, let’s take a detail look at the datapath during various phase of this instruction.
+2 = 10 min. (X:50)

## Slide 22: Instruction Fetch Unit start of Add
Fetch the instruction from Instruction memory:
  Instruction = MEM[PC]
  same for all instructions
imm16
clk
PC
00
4
nPC_sel
PC Ext
Adder
Adder
Mux
Inst Address
Inst
Memory
Instruction<31:0>

## Slide 23: The Single Cycle Datapath during Add
R[rd] = R[rs] + R[rt]
op
rs
rt
rd
shamt
funct
0
6
11
16
21
26
31
32
ALUctr=ADD
clk
busW
RegWr=1
32
32
busA
32
busB
5
5
Rw
Ra
Rb
RegFile
Rs
Rt
Rt
Rd
RegDst=1
Extender
32
16
imm16
ALUSrc=0
ExtOp=x
MemtoReg=0
clk
Data In
32
MemWr=0
zero
0
1
0
1
=
ALU
0
1
WrEn
Adr
Data
Memory
5
Instruction<31:0>
<21:25>
<16:20>
<11:15>
<0:15>
Imm16
Rd
Rt
Rs
nPC_sel=+4
instr
fetch
unit
clk
Notes: This picture shows the activities at the main datapath during the execution of the Add or Subtract instructions.
The active parts of the datapath are shown in different color as well as thicker lines.
First of all, the Rs and Rt of the instructions are fed to the Ra and Rb address ports of the register file and cause the contents of registers specified by the Rs and Rt fields to be placed on busA and busB, respectively.
With the ALUctr signals set to either Add or Subtract, the ALU will perform the proper operation and with MemtoReg set to 0, the ALU output will be placed onto busW.
The control we are going to design will also set RegWr to 1 so that the result will be written to the register file at the end of the cycle.
Notice that ExtOp is don’t care because the Extender in this case can either do a SignExt or ZeroExt. We DON’T care because ALUSrc will be equal to 0--we are using busB.
The other control signals we need to worry about are:
(a) MemWr has to be set to zero because we do not want to write the memory.
(b) And Branch and Jump, we have to set to zero. Let me show you why.
+3 = 15 min. (X:55)

## Slide 24: Instruction Fetch Unit end of Add
PC = PC + 4
  This is the same for all instructions except: Branch and Jump
imm16
clk
PC
00
4
nPC_sel=0
PC Ext
Adder
Adder
Mux
Inst Address
Inst
Memory
Next PC address
New instruction
0
1
Notes: This picture shows the control signals setting for the Instruction Fetch Unit at the end of the Add or Subtract instruction.
Both the Branch and Jump signals are set to 0.
Consequently, the output of the first adder, which implements PC plus 1, is selected through the two 2-to-1 mux and got placed into the input of the Program Counter register.
The Program Counter is updated to this new value at the next clock tick.
Notice that the Program Counter is updated at every cycle. Therefore it does not have a Write Enable signal to control the write.
Also, this picture is the same for or all instructions other than Branch andJjump.
Therefore I will only show this picture again for the Branch and Jump instructions and will not repeat this for all other instructions.
+2 = 17 min. (X:57)

## Slide 25
op
rs
rt
immediate
0
16
21
26
31
R[rt] = R[rs] OR ZeroExt[Imm16]
32
ALUctr=
clk
busW
RegWr=
32
32
busA
32
busB
5
5
Rw
Ra
Rb
RegFile
Rs
Rt
Rt
Rd
RegDst=
Extender
32
16
imm16
ALUSrc=
ExtOp=
MemtoReg=
clk
Data In
32
MemWr=
zero
0
1
0
1
=
ALU
0
1
WrEn
Adr
Data
Memory
5
Instruction<31:0>
<21:25>
<16:20>
<11:15>
<0:15>
Imm16
Rd
Rt
Rs
nPC_sel=
instr
fetch
unit
clk
Single Cycle Datapath for Ori
Notes: Now let’s look at the control signals setting for the Or immediate instruction.
The OR immediate instruction OR the content of the register specified by the Rs field to the Zero Extended Immediate field and write the result to the register specified in Rt.
This is how it works in the datapath. The Rs field is fed to the Ra address port to cause the contents of register Rs to be placed on busA.
The other operand for the ALU will come from the immediate field. In order to do this, the controller need to set ExtOp to 0 to instruct the extender to perform a Zero Extend operation.
Furthermore, ALUSrc must set to 1 such that the MUX will block off bus B from the register file and send the zero extended version of the immediate field to the ALU.
Of course, the ALUctr has to be set to OR so the ALU can perform an OR operation.
The rest of the control signals (MemWr, MemtoReg, Branch, and Jump) are the same as theAdd and Subtract instructions.
One big difference is the RegDst signal. In this case, the destination register is specified by the instruction’s Rt field, NOT the Rd field because we do not have a Rd field here.
Consequently, RegDst must be set to 0 to place Rt onto the Register File’s Rw address port.
Finally, in order to accomplish the register write, RegWr must be set to 1.
+3 = 20 min. (X:60)

## Slide 26: Single Cycle Datapath for Ori
R[rt] = R[rs] OR ZeroExt[Imm16]
op
rs
rt
immediate
0
16
21
26
31
32
ALUctr=OR
clk
busW
RegWr=1
32
32
busA
32
busB
5
5
Rw
Ra
Rb
RegFile
Rs
Rt
Rt
Rd
RegDst=0
Extender
32
16
imm16
ALUSrc=1
ExtOp=zero
MemtoReg=0
clk
Data In
32
MemWr=0
zero
0
1
0
1
=
ALU
0
1
WrEn
Adr
Data
Memory
5
Instruction<31:0>
<21:25>
<16:20>
<11:15>
<0:15>
Imm16
Rd
Rt
Rs
nPC_sel=+4
instr
fetch
unit
clk
Notes: Now let’s look at the control signals setting for the Or immediate instruction.
The OR immediate instruction OR the content of the register specified by the Rs field to the Zero Extended Immediate field and write the result to the register specified in Rt.
This is how it works in the datapath. The Rs field is fed to the Ra address port to cause the contents of register Rs to be placed on busA.
The other operand for the ALU will come from the immediate field. In order to do this, the controller need to set ExtOp to 0 to instruct the extender to perform a Zero Extend operation.
Furthermore, ALUSrc must set to 1 such that the MUX will block off bus B from the register file and send the zero extended version of the immediate field to the ALU.
Of course, the ALUctr has to be set to OR so the ALU can perform an OR operation.
The rest of the control signals (MemWr, MemtoReg, Branch, and Jump) are the same as theAdd and Subtract instructions.
One big difference is the RegDst signal. In this case, the destination register is specified by the instruction’s Rt field, NOT the Rd field because we do not have a Rd field here.
Consequently, RegDst must be set to 0 to place Rt onto the Register File’s Rw address port.
Finally, in order to accomplish the register write, RegWr must be set to 1.
+3 = 20 min. (X:60)

## Slide 27
R[rt] = Data Memory {R[rs] + SignExt[imm16]}
op
rs
rt
immediate
0
16
21
26
31
32
ALUctr=
clk
busW
RegWr=
32
32
busA
32
busB
5
5
Rw
Ra
Rb
RegFile
Rs
Rt
Rt
Rd
RegDst=
Extender
32
16
imm16
ALUSrc=
ExtOp=
MemtoReg=
clk
Data In
32
MemWr=
zero
0
1
0
1
=
ALU
0
1
WrEn
Adr
Data
Memory
5
Instruction<31:0>
<21:25>
<16:20>
<11:15>
<0:15>
Imm16
Rd
Rt
Rs
nPC_sel=
instr
fetch
unit
clk
Single Cycle Datapath for LW
Notes: Let’s continue our lecture with the load instruction. What does the load instruction do?
It first adds the contecnts of the register specified by the Rs field to the Sign Extended version of the Immediate field to form the memory address.
Then it uses this memory address to access the memory and write the data back to the register specified by the Rt field of the instruction.
Here is how the datapath works: first the Rs field is fed to the Register File’s Ra address port to place the register onto bus A.
Then the ExtOp signal is set to 1 so that the immediate field is Sign Extended and we place this value (output of Extender) onto the ALU input by setting ALUsrc to 1.
The ALU then add (ALUctr = add) the two together to form the memory address which is then placed onto the Data Memory’s address port.
In order to place the Data Memory’s output bus onto the Register File’s input bus (busW), the control needs to set MemtoReg to 1.
Similar to the OR immediate instruction I showed you earlier, the destination register here is specified by the Rt field. Therefore RegDst must be set to 0.
Finally, RegWr must be set to 1 to completer the register write operation.
Well, it should be obvious to you guys by now that we need to set Branch and Jump to 0 to make sure the Instruction Fetch Unit update the Program Counter correctly.
+3 = 28 min. (Y:08)

## Slide 28: Single Cycle Datapath for LW
R[rt] = Data Memory {R[rs] + SignExt[imm16]}
op
rs
rt
immediate
0
16
21
26
31
32
ALUctr=ADD
clk
busW
RegWr=1
32
32
busA
32
busB
5
5
Rw
Ra
Rb
RegFile
Rs
Rt
Rt
Rd
RegDst=0
Extender
32
16
imm16
ALUSrc=1
ExtOp=sign
MemtoReg=1
clk
Data In
32
MemWr=0
zero
0
1
0
1
=
ALU
0
1
WrEn
Adr
Data
Memory
5
Instruction<31:0>
<21:25>
<16:20>
<11:15>
<0:15>
Imm16
Rd
Rt
Rs
nPC_sel=+4
instr
fetch
unit
clk
Notes: Let’s continue our lecture with the load instruction. What does the load instruction do?
It first adds the contecnts of the register specified by the Rs field to the Sign Extended version of the Immediate field to form the memory address.
Then it uses this memory address to access the memory and write the data back to the register specified by the Rt field of the instruction.
Here is how the datapath works: first the Rs field is fed to the Register File’s Ra address port to place the register onto bus A.
Then the ExtOp signal is set to 1 so that the immediate field is Sign Extended and we place this value (output of Extender) onto the ALU input by setting ALUsrc to 1.
The ALU then add (ALUctr = add) the two together to form the memory address which is then placed onto the Data Memory’s address port.
In order to place the Data Memory’s output bus onto the Register File’s input bus (busW), the control needs to set MemtoReg to 1.
Similar to the OR immediate instruction I showed you earlier, the destination register here is specified by the Rt field. Therefore RegDst must be set to 0.
Finally, RegWr must be set to 1 to completer the register write operation.
Well, it should be obvious to you guys by now that we need to set Branch and Jump to 0 to make sure the Instruction Fetch Unit update the Program Counter correctly.
+3 = 28 min. (Y:08)

## Slide 29
op
rs
rt
immediate
0
16
21
26
31
Data Memory {R[rs] + SignExt[imm16]} = R[rt]
32
ALUctr=
clk
busW
RegWr=
32
32
busA
32
busB
5
5
Rw
Ra
Rb
RegFile
Rs
Rt
Rt
Rd
RegDst=
Extender
32
16
imm16
ALUSrc=
ExtOp=
MemtoReg=
clk
Data In
32
MemWr=
zero
0
1
0
1
=
ALU
0
1
WrEn
Adr
Data
Memory
5
Instruction<31:0>
<21:25>
<16:20>
<11:15>
<0:15>
Imm16
Rd
Rt
Rs
nPC_sel=
instr
fetch
unit
clk
Single Cycle Datapath for SW
Notes: The store instruction performs the inverse function of the load. Instead of loading data from memory, the store instruction sends the contents of register specified by Rt to data memory.
Similar to the load instruction, the store instruction needs to read the contents of register Rs (points to Ra port) and add it to the sign extended verion of the immediate filed (Imm16, ExtOp = 1, ALUSrc = 1) to form the data memory address (ALUctr = add).
However unlike the Load instructoion where busB is not used, the store instruction will use busB to send the data to the Data memory.
Consequently, the Rt field of the instruction has to be fed to the Rb port of the register file.
In order to write the Data Memory properly, the MemWr signal has to be set to 1.
Notice that the store instruction does not update the register file. Therefore, RegWr must be set to zero and consequently control signals RegDst and MemtoReg are don’t cares.
And once again we need to set the control signals Branch and Jump to zero to ensure proper Program Counter updataing.
Well, by now, you are probably tied of these boring stuff where Branch and Jump are zero so let’s look at something different--the bracnh instruction.
+3 = 31 min. (Y:11)

## Slide 30: Single Cycle Datapath for SW
Data Memory {R[rs] + SignExt[imm16]} = R[rt]
op
rs
rt
immediate
0
16
21
26
31
32
ALUctr=ADD
clk
busW
RegWr=0
32
32
busA
32
busB
5
5
Rw
Ra
Rb
RegFile
Rs
Rt
Rt
Rd
RegDst=x
Extender
32
16
imm16
ALUSrc=1
ExtOp=sign
MemtoReg=x
clk
Data In
32
MemWr=1
zero
0
1
0
1
=
ALU
0
1
WrEn
Adr
Data
Memory
5
Instruction<31:0>
<21:25>
<16:20>
<11:15>
<0:15>
Imm16
Rd
Rt
Rs
nPC_sel=+4
instr
fetch
unit
clk
Notes: The store instruction performs the inverse function of the load. Instead of loading data from memory, the store instruction sends the contents of register specified by Rt to data memory.
Similar to the load instruction, the store instruction needs to read the contents of register Rs (points to Ra port) and add it to the sign extended verion of the immediate filed (Imm16, ExtOp = 1, ALUSrc = 1) to form the data memory address (ALUctr = add).
However unlike the Load instructoion where busB is not used, the store instruction will use busB to send the data to the Data memory.
Consequently, the Rt field of the instruction has to be fed to the Rb port of the register file.
In order to write the Data Memory properly, the MemWr signal has to be set to 1.
Notice that the store instruction does not update the register file. Therefore, RegWr must be set to zero and consequently control signals RegDst and MemtoReg are don’t cares.
And once again we need to set the control signals Branch and Jump to zero to ensure proper Program Counter updataing.
Well, by now, you are probably tied of these boring stuff where Branch and Jump are zero so let’s look at something different--the bracnh instruction.
+3 = 31 min. (Y:11)